## Slide 1: VW
1D bar example

## Slide 2: Problem setup: 1D linear elastic bar subjected to point and body loads

## Slide 3: Problem setup: 1D linear elastic bar subjected to point and body loads

## Slide 4: Principle of Virtual Work
According to the PVW, for any mechanical system under the state of equilibrium, total virtual work done by external and internal forces for any arbitrarily small non-zero virtual displacement should be zero.

## Slide 5: A primitive version for the expression of virtual work is obtained by substituting the domain volume expression in 1D.
To capture the mechanical response, we need additional information such as constitutive equation, which defines the material response of the underlying continuum. Secondly, we also need kinematic equation relating strain ε to displacement function u(x).

## Slide 6: a weak form gets it’s name because the unknown field variable u(x) has to satisfy the mechanical balance law defining the problem only in an averaged sense/weak sense over the entire domain — due to the presence of an integral sign over the entire domain.

## Slide 7: Estimation of unknown field variable u(x)

## Slide 8: Basic idea behind discretization using finite element method

## Slide 9: To estimate unknown displacement in 1D bar, we conceptualize a linear 1D finite element with 2 nodes, which can take loads only in the axial direction, hence it has 1 degree of freedom per node and thus total 2 degrees of freedom. To make calculations easy a local element coordinate system has been introduced, which varies between -1 and 1, with origin at the centre of the finite element. This finite element can take external nodal loads as well as body loads distributed over it’s length.

## Slide 10: Matrix representation of displacement and strain in 1D linear finite element
Since the finite element is linear with just two nodes, we have two shape functions (N1, N2) and two unknown nodal displacement values (d1, d2). Thus, shape function matrix N has dimensions 1x2 and displacement vector d has dimensions 2x1. Their scalar product results in a scalar displacement function for the case of 1D domain.

## Slide 11: …

## Slide 12: Isoparametric concept in finite element analysis
According to the Isoparametric concept in finite element analysis, the shape functions which are used on an element to approximate unknown field variable are also used to approximate the geometry of a given finite element.

## Slide 13: It becomes essential to transfer the stiffness matrix integration from global to local coordinate system. This is done by using the concept of Jacobian which was introduced earlier.

## Slide 14: Finally

## Slide 15: Problem boundary conditions — Dirichlet and Neumann

## Slide 16: To establish the connectivity between all the elements at their respective common nodes, we define a so-called topology matrix which contains information about which degrees of freedom are associated with which elements.

## Slide 17: To establish a relationship between local element coordinate system and global coordinate x, we consider a random finite element number n. The left node of this element has coordinates of (n-1)*le and right node has the coordinate n*le. Using Isoparametric concept, x coordinate/position at any point within this element can be established as shown below.

## Slide 18: Assembly

## Slide 20: Back calculation of individual element force